## Slide 1: emBO++ 2019
embedded C++
for
embedded C programmers
Wouter van Ooijen MSc (ir)
Hogeschool Utrecht, Netherlands,
senior lecturer Computer Engineering
SG14 member
wouter.vanooijen@hu.nl
Notes: Wouter van Ooijen, if too difficult Woooter will do
Backgroundf Computer Science, passion electronics and hardware/software borderland
Polytechnics
Technical Informatics, small specialization~30-50 std annually
I am NOT working in industry, I guide the next generations into inductry. I hope well prepared

## Slide 3: Agenda
Define ‘embedded’
From C to C++
Hwlib: my C++ embedded OO library

## Slide 4
embedded

## Slide 5
Wide span of seriousness
fun
deadly serious
Notes: Furby to nuclear power plant

## Slide 6
Wide span of response time
µs
ms
s
Notes: Nuclear doesn’t require that qiock responses

## Slide 7
1MiB
1GiB
1KiB
4-bit
8-bit : 8051, PIC, AVR, …
16-bit : MSP430, PIC, …
64-bit
No full standard C/C++
32-bit : ARM, MIPS, Tensilca, Intel, …
Wide span of hardware

## Slide 8
Wide span of support software
Bare metal:
libraries
no separate OS
1MiB
1GiB
1KiB
Desktop OS:
Linux
Windows
Interpreter
RTOS

## Slide 9
large-embedded
small-embedded
fast trading
gaming
simulation
MiB, GiB
GHz, multi-core
Memory latency, caches
bytes, KiB
MHz, Interrupts
Hardware peripherals
Battery life-time

## Slide 10
1MiB
1GiB
1KiB
‘my’ embedded
Bare metal, no (separate) OS
Kb RAM and ROM (not Mb)

## Slide 11: Embedded languages
Probably not my type of embedded

## Slide 12
C  C++

## Slide 14: Face the opposition: reasons to stick to C
Some good ones
Some debatable ones
Some bad ones

## Slide 15: Stick to C : some good reasons
No (good, mandated, … ) C++ compiler available
C is required (by the customer, law, insurance, … )
Your code relies on Variable Length Arrays

## Slide 16: GCC targets
Missing?
PIC
8051
AVR library support is minimal
No (good, mandated, … ) C++ compiler available
C is required (by the customer, law, insurance, … )
Your code relies on Variable Length Arrays

## Slide 17
C
No (good, mandated, … ) C++ compiler available
C is required (by the customer, law, insurance, … )
Your code relies on Variable Length Arrays

## Slide 18: Variable Length Array
Mandatory in C99, optional in later versions
Not in standard C++
Available in GCC as an extension
void f( int n ){
int array[n];
. . .
}
No (good, mandated, … ) C++ compiler available
C is required (by the customer, law, insurance, … )
Your code relies on Variable Length Arrays

## Slide 19: Why use C : some temporary reasons
large existing C code base
no C++ programmers available
no guidelines, books, courses, etc. for C++

## Slide 20: Don’t throw your C away!
large existing C code base
no C++ programmers available
no guidelines, books, courses, etc. for C++
start with the lowest ambition: compile your C as C++

## Slide 21: No C++ programmers available
large existing C code base
no C++ programmers available
no guidelines, books, courses, etc. for C++
ask your programmers, you might be surprised
get some (good luck…)
get training
begin with the small steps

## Slide 22: No guidelines, books, courses, …
large existing C code base
no C++ programmers available
no guidelines, books, courses, etc. for C++
again, start with the small steps
there is some material & experience
communicate!

## Slide 23: Why use C : some debatable reasons
C++ is larger, hence code is less easy to read
C++ makes code execution less predictable (debug)

## Slide 24: Yes, C++ is large
C++ is larger, hence code is less easy to read
C++ makes code execution less predictable (debug)

## Slide 25: Development styles
EE / C – style
See what you do – down to assembly
Write quickly, you’ll need the time later on for debugging
The effect is what you observe (UB is just another compiler feature)
If it works, don’t touch it
Big vendor selling points: debuggers, generators
CS / C++ - style
Build and use abstractions that you trust
Write carefully, review, test
The effect is what it should be (no UB allowed)
If the source is not right, correct it (and re-test)
I don’t even have a debugger for any of the chips I use…
C++ is larger, hence code is less easy to read
C++ makes code execution less predictable (debug)

## Slide 26: Why use C : some bad reasons
C++ is slower
C++ produces larger executables
 Use your toolchain appropriately

## Slide 27: Strategies

## Slide 28: Cold Turkey : start a new project in C++
Get the right people (might be tricky):
Don’t rely on C-style EE’s
Don’t rely on C++-desktop style CS’s.
Fresh students, hobbyists, outside help, …
 Don’t feel obliged to use the full language!

## Slide 29: C++ features to avoid
(probably) avoid:
RTTI
the heap (free store), hence
exceptions
standard containers (except std::array<>)
floating point

## Slide 30: Salami technique : small steps first (world domination has to wait)
Low-impact (don’t disturb the C-culture too much)
Medium-impact (expect some resistance..)
OO (familiar to non-embedded C++ programmers)
Modern (keep an expert nearby)

## Slide 31: Low-impact C++ features
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 32: const correctness
A const is read-only.
In C, ”abcd” is a (non-const) char pointer
void clear( char * s ){
s[ 0 ] = ’\0’;
}
clear( ”Hello world” );
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 33: Binary literals
The first purpose of code is to be readable.
The base you choose conveys information about the value.
Some values are simply bits.
0b1011 // a bit mask
083 // not written by me
0x0B // a value, but not for a calculation
11 // the quantity 11
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 34: ’ separators in literals
I can’t quickly read numbers with a large number of digits.
Can you?
wait_ns ( 1000000000 ); // one second (if I got the 0’s right)
wait_ns ( 1000 * 1000 * 1000 ); // don’t worry, it’s a ct-expression
wait_ns ( 1’000’000’000 );
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 35: namespaces
// C style
mygreatlibrary_importantfunction{ ... }
// C++ style
namespace mygreatlibrary {
void importantfunction(){ . . . }
};
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 36: namespaces
// C style
mygreatlibrary_importantfunction();
// or
using namespace mygreatlibrary;
importantfunction();
// C++ style
mygreatlibrary::importantfunction();
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 37: Enum class
// C style / old C++ style
enum color { color_black, color_white, color_red, ... };
enum player { player_white, player_black };
void paint( color c );
paint( player_white );
// new C++ style
enum color { black, white, red, ... };
enum player { white, black };
void paint( color c );
paint( white ); // compiler error
paint( player::white ); // compiler error
paint( color::white );
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 38: By-reference parameters
// C style
void inc( int * p ){
*p++; // did I get that right?
}
int n;
inc( &n );
// C++ style
void inc( int & p ){
p++;
}
int n;
inc( n ); // some C folks find this annoying
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 39: constexpr
Most micro-controllers have 4-16 times more FLASH than RAM.
A value in FLASH can’t accidentally be overwritten.
Calculating (even at start-up) takes time (and FLASH).
I am no good at excel and cut-n-paste.
 I want as much in FLASH as possible!
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 40: constexpr
constexpr double pow( double v, int n ){
return ( n == 0 )
? 1
: v * pow( v, n - 1 );
}
constexpr int fac( int n ){
return ( n == 0 )
? 1
: n * fac( n - 1 );
}
constexpr double sine( double angle ){
double value = 0;
for( int i = 1; i < 10; i += 2 ){
value += (( i % 4 ) == 1 ? 1 : -1 ) * pow( angle, i ) / fac( i );
}
return value;
}
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 41: constexpr
no run-time calculation
no floating-point code linked in!
constexpr double pi = 3.14;
constexpr int height = static_cast< int >( 1000 * sine( 2 * pi / 12 ));
int main( void ){
// wait for the terminal emulator to start up
hwlib::wait_ms( 1'000 );
hwlib::cout << "1000 * sin( 30 ) = " << height << "\n";
}
const correctness
binary literals
’ separator in literals
namespaces
enum class
by-reference parameters
constexpr
if constexpr

## Slide 42: Medium-impact C++ features
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)

## Slide 43: Overloading
Seems to be a very personal thing
// C style
print_int( 42 );
print_double( 3.14 );
print_string( ”Hello” );
// C++ style
print( 42 );
print( 3.14 );
print( ”Hello” );
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)

## Slide 44: Default parameters
Also seems to be a very personal thing
// C style
print( 42 ); // 42
print_in_field( 42, -1 ); // 42
print_in_field( 42, 5 ); // ===42
// C++ style
print( int x, int p = -1 );
print( 42 ); // 42
print( 42, 5 ); // ===42
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)

## Slide 45: Transparent data types
I hate adjacent parameters of the same type
write( int x, int y, bool v );
write( x, y, 1 );
write( x + 1, y + 1, 0 );
struct xy { int x, int y, ... };
write( loc );
write( loc + xy( 1, 1 ), 0 );
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)

## Slide 46
int main( void ){
. . .
auto lcd = hwlib::hd44780( rs, e, d, hwlib::xy( 2, 16 ) );
lcd
<< "\fHello world!"
<< hwlib::flush;
}

## Slide 47
int main( void ){
. . .
auto lcd = hwlib::hd44780( rs, e, d, hwlib::xy( 16, 2 ) );
lcd
<< "\fHello world!"
<< hwlib::flush;
}

## Slide 48: Abstract data types
int distance = 3246; // in miles
int d; // duration in seconds
d = distance; // oops!
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)

## Slide 49
#include <iostream>
#pragma GCC diagnostic ignored "-Wparentheses"
#pragma GCC optimize ("rtti")
#include <boost/units/systems/si.hpp>
#include <boost/units/systems/cgs/length.hpp>
#include <boost/units/io.hpp>
const auto meter = 1.0 * boost::units::si::meter;
const auto s = 1.0 * boost::units::si::second;
void print( decltype( meter / s ) v ){
std::cout << "velocity = " << v << "\n";
}
int main(){
auto gravity = 10.0 * meter / ( s * s );
auto duration = 2.0 * s;
print( gravity * duration );
}
Overloading
Default parameters
Transparent Data Types
Abstract Data Types (private)
documentation?
errors 

## Slide 50: OO C++ features
basic OO: interface, with different implementations
decorators / adapters (run-time composition)
for( : )
auto
} (destructors)

## Slide 51: OO: a class is just a struct
class xy {
public:
int x, y;
xy( int x, int y ): x( x ), y( y ){}
xy add( xy rhs ){
return xy( x + rhs.x, y + rhs.y );
}
};
auto a = xy( 1, 2 );
auto b = xy( 3, 4 );
auto c = a.add( b );
struct xy {
int x, y;
};
xy add( xy * this_, xy rhs ){
return xy{
this_->x + rhs.x,
this_->y + rhs.y };
}
xy a{ 1, 2 };
xy b{ 3, 4 };
xy c = add( &a, b );

## Slide 52: OO: virtuals are just function pointers
class xy {
public:
int x, y;
xy( int x, int y ): x( x ), y( y ){}
virtual void print() = 0;
};
class my_xy : public xy {
public:
my_xy( int x, int y ): xy( x, y ){}
void print() override {
std::cout << "[" << x << "," << y << "]"; }
};
void f(){
auto a = my_xy( 1, 2 );
a.print();
}
struct xy_functions;
struct xy {
int x, y;
const xy_functions *vft;
xy( int x, int y, const xy_functions *vft ):
x( x ), y( y ), vft( vft ){}
};
struct xy_functions {
void (*print)( xy * );
};
void my_xy_print( xy * this_){
std::cout<< "[" << this_->x << "," << this_->y << "]";
};
const xy_functions my_xy_vft = { my_xy_print };
struct my_xy : xy {
my_xy( int x, int y ): xy( x, y, & my_xy_vft ){}
};
void f(){
auto a = my_xy( 42, 84 );
(( xy_functions * ) a.vft )->print( & a );
}

## Slide 53: One interface, multiple implementations

## Slide 54: Adapter: one interface on top of another one

## Slide 55: Decorator: modified semantics over the same interface

## Slide 56: for

## Slide 57: destructors

## Slide 58: Modern C++ features
Templated interfaces
Domain Specific Languages
Compile-time composition (CRTP)
Real Magic (Odin, Chiel, …)

## Slide 59
Hwlib

## Slide 60
HBO-ICT

## Slide 62
Q1
Programming (Python)
Computer systems & networks
ICT and organization
Q2
Modelling (BPMN, use-cases, databases)
ASK (Critical thinking, logics, statistics)
Group project (collaboration, agile, professional skills)
Q3
procedural programming (algorithmics, C++)
operating systems (Linux, RaPi)
Lego Robotics (Lego + BrickPi, C++)
Q4
OO programming and micro-controllers (classic C++, ArduinoDue)
Digital and analog electronics, computer architecture
1st year final project (individual, ArduinoDue, C++)

## Slide 63
Q5
Low-level programming (assembly, C++, threading)
Real-time modelling (UML & synchronization)
Laser-Tag project (RTOS, modelling, waterfall, C++)
Q6
High-level programming (C++, resources, STL, patterns, SFML)
Datastructures & algorithms (lists, trees, hashmaps; Python)
Game project (SFML, PC/Linux/Mac, Agile/scrum, C++)
Q7
MRB (sensors, actuators, control)
Vision (image processing)
Development department: large group, proposals, dependencies
continuous integration, tests, changing requirements, self-organizing,
scrum
Q8
Research
Development department cont. – 15 EC total

## Slide 64: A manufacturers perspective:
High-volume developer / manufacturer
  Keep ‘m hooked!
  dedicated IDE, toolchain, code generator, etc.
Low-volume developer / education / hobby
   not very insteresting

## Slide 65: A teachers perspective:
I don’t care much which target is used, but it must be
Cheap
Available for a long time
Be a Cortex (-M) (for the assembler lessons)
I want to be able to switch targets easily.

## Slide 66: Steps for micro-controller development:
Write the code
Compile
Link on your host system (Windows, Mac, Linux)
Download to the target system
Run on the target system
Observe the effects, goto step 1

## Slide 67: Resources for micro-controller development:
Cross-toolchain (compiler & linker)
Language library & runtime (standalone subset…)
Chip headers
Chip startup code
Chip linker script
Download tool
Download hardware
Target system

## Slide 68: What I use / provide
GCC
Cross-toolchain
Language library & runtime
Chip headers
Chip startup code
Chip linker script
Download tool
Download hardware
Target system
Hwlib
bmptk
www.github.com/wovo/bmptk
Arduino Due

## Slide 69: (other) Interesting targets:
AVR8 (AtMega328P, Arduino Uno/Nano/Micro, has issues)
(MSP430: to prove that 16-bit still exists)
Cortex-M (Arduino Due, Blue Pill, lots of manufacturer boards)
(Tensilica: ESP8266, ESP32)
(MIPS: Microchip, 32-bit DIP micro-controllers)
(Cortex-A: Pi bare-metal)

## Slide 70: Hwlib: embedded OO library
Used in classes, so:
Use what the students know (OO syntax, no templates)
Don’t provide what they can make themselves
Solving already solved problems is not a problem
www.github.com/wovo/hwlib

## Slide 71: Hwlib
Some available abstractions:
Timing (wait, time-of-day)
GPIO pin, GPIO port (bunch of pins)
ADC, DAC
I2C, SPI
Character I/O
Graphics

## Slide 72: Hwlib - some available implementations
HAL for AVR8 (uno) and some Cortex-M (due, blue-pill)
Bit-banged UART, I2C, SPI
PCF8591, PCD8574, HC595
HD44780 (char LCD), SSD1306 (graphic OLED)

## Slide 73: Hwlib
Some available ‘layers’:
Pin & port decorators/adapters/creators
Graphics
Character terminal, also on graphics
Multi-threading (separate library)

## Slide 74: Let’s blink a LED!

## Slide 75: GPIO
Internal circuit

## Slide 76: GPIO
Protection

## Slide 77: GPIO
Output circuit

## Slide 78: GPIO
Input circuit

## Slide 79: GPIO
Pull-up / pull-down circuit

## Slide 80: atMega328 (Arduino Uno)

## Slide 81: Blink : atMega328 (Arduino Uno)
#include "hwlib.hpp"
int main( void ){
DDRB |= ( 0b01 << 5 );
for(;;){
PORTB &= ~( 0b01 << 5 );
for( volatile uint32_t i = 0; i < 50'000; ++i );
PORTB |= ( 0b01 << 5 );
for( volatile uint32_t i = 0; i < 50'000; ++i );
}
}

## Slide 82: STM32F103 (Blue Pill)

## Slide 83: Blink : STM32F103 (Blue Pill)
#include "hwlib.hpp"
int main( void ){
GPIOB->CRH &= ~( 0xF << ( 5 * 4 ));
GPIOB->CRH |= 0x03 << ( 5 * 4 );
for(;;){
GPIOB->BSRR |= ( 0x01 << 13 );
for( volatile uint32_t i = 0; i < 10'000; i++ ){}
GPIOB->BSRR |= ( 0x01 << ( 13 + 16 ));
for( volatile uint32_t i = 0; i < 10'000; i++ ){}
}
}

## Slide 84: ATSAM3X8E (Arduino Due)

## Slide 85: Blink : ATSAM3X8E (Arduino Due)
#include "hwlib.hpp"
int main( void ){
PIOB->PIO_OER = { 0x1U << 27 };
for(;;){
PIOB->PIO_SODR = 0x01 << 27;
for( volatile uint32_t i = 0; i < 100'000; i++ ){}
PIOB->PIO_CODR = 0x01 << 27;
for( volatile uint32_t i = 0; i < 100'000; i++ ){}
}
}

## Slide 86: Blink - abstraction
int main( void ){
auto led = hwlib::target::pin_in_out( 1, 5 );
led.direction_set_output();
for(;;){
led.write( 1 ); led.flush();
hwlib::wait_ms( 100 );
led.write( 0 ); led.flush();
hwlib::wait_ms( 100 );
}
}

## Slide 87: Blink – more abstraction
int main( void ){
auto led = hwlib::target::pin_in_out( 1, 5 );
led.direction_set_output();
for(;;){
led.write( 1 ); led.flush();
hwlib::wait_ms( 100 );
led.write( 0 ); led.flush();
hwlib::wait_ms( 100 );
}
}
int main( void ){
auto pin = hwlib::target::pin_out( 1, 5 );
auto led = hwlib::direct( pin );
for(;;){
led.write( 1 );
hwlib::wait_ms( 100 );
led.write( 0 );
hwlib::wait_ms( 100 );
}
}

## Slide 88: GPIO pin: types / modes of use
Input
Output
Input-Output
Open-Collector
Pull-up, pull-down

## Slide 89: GPIO pins: HAL-provided
auto pin = hwlib::target::pin_in_out( 1, 5 );
auto pin = hwlib::target::pin_in( 1, 5 );
auto pin = hwlib::target::pin_out( 1, 5 );
auto pin = hwlib::target::pin_oc( 1, 5 );

## Slide 90: GPIO pin: adapters/decorators
auto pin = hwlib::target::pin_in_out( 1, 5 );
auto p = hwlib::pin_in_from( pin );
auto p = hwlib::pin_out_from( pin );
auto p = hwlib::pin_oc_from( pin );
auto d = hwlib::direct( p );
auto i = hwlib::invert( d );

## Slide 91: Ports: bundle of pins
auto p19 = hwlib::target::pin_out( 1, 9 );
. . .
auto scl = hwlib::target::pin_out{ 0, 4 };
auto leds = hwlib::port_out_from_pins(
p19, p18, p15, p14,
p13, p12, p11, p10,
p07, p06, sda, scl
);

## Slide 92: Ports: adapters/decorators
auto port = hwlib::port_in_out_from_pins( . . . );
auto p = hwlib::port_in_from( pin );
auto p = hwlib::port_out_from( pin );
auto d = hwlib::direct( p );
auto i = hwlib::invert( d );
auto a = hwlib::all( p );

## Slide 93: Three demo functions
blink( pin );
kitt( port );
snake( port );

## Slide 95
Some experiences
Getting abstractions right is difficult
 we need more communication
Working with classes (instead of objects) is much easier
Documentation tools (Doxygen etc.) are not up to it

## Slide 97
Takeaways
If you switch to C++, don’t feel obliged to
go cold turkey (small steps are perfectly OK)
use the whole language (you didn’t use full C either!)
Even old-school OO can be usefull for smal-embedded.