## Slide 1
Wouter van Ooijen
wouter@voti.nl
MicroPython
https://micropython.org
MicroPython

## Slide 2
Questions are welcome

## Slide 3
Programmer by profession, electronics tinkerer by passion
Wouter van Ooijen
wouter@voti.nl
Me
TU Delft Informatica 1988
ICT Automatisering
  VAX11 industrial datacommunication
  @ Fokker Space / Dutch Space: Era Robotic ARM
  @ Hollandse Signaal / Thales: SmartNet ATM datacommunications system
VOTI webshop, self-employed (NLR), projects
Hogeschool Utrecht: lecturer Technische Informatica
  C, C++, assembler, Python, SE, electronics, Java
Cboost
  C++ and embedded specialist

## Slide 4
Micro-processor
A micro-processor is:
CPU only
What is in your desktop, laptop, server, mobile
$$$
Optimized for processing power
Uses external ROM, RAM, peripherals, ...
Needs LOTS of power (and often cooling)
faster
1971
0.1 MIPS
4 bits
2023
300 GIPS
64 bits

## Slide 5
Micro-controller
A micro-controller is
A single* chip with CPU, RAM, FLASH, I/O, …
Cheap, small, low-power
Used for embedded, real-time
(Much) less resources than a desktop
What you find in almost everything that is not a computer
Include more
(OK, a bit faster too)
1971
just the CPU
2023
CPU, MMU
ROM, RAM
GPIO, A/D, D/A
I2C, SPI, I2S
….

## Slide 6
Translates
Runs
Compiler
Source code
CPU
Compiler
Application
Runs
interaction

## Slide 7
Interprets
Runs
Interpreter
Source code
CPU
Interpreter
interaction

## Slide 8
Interprets
Runs
Compiler / Interpreter
Source code
CPU
Compiler
Translates
Interpreter / Virtual Machine
Runs
Intermediate code
interaction

## Slide 9
(C)Python
Source code
CPU

## Slide 10
Thonny
MicroPython
On the PC
Desktop CPU
MicroPython
MicroController
On the MC
REPL

## Slide 11
(Micro)Python REPL
Read-Evaluate-Print Loop:
Connects to your PC via serial-over-USB*
Read your input
Evaluate (run) it
Print the result
Repeat this forever
Acts as a primitive Operating System command interpreter
Provides a simple file system
Can interrupt a running program

## Slide 12
Thonny
Simple Python edit-run IDE
Can be configured to run remotely via REPL over (USB-) serial
Has very simple but useable file system views, with upload / download *
Can directly install MicroPython on some target chips
Editor is a bit primitive (I prefer Notepad++ for serious editing work)

## Slide 13
Demo install
Install by hand:
  Connect Pi Pico USB while button pressed
  RPI-RP (D:) drive shows up in explorer
  Copy MicroPython image file to RPI-RP (D:)
Install using Thonny:
  Again, Connect Pi Pico USB while button pressed
  InThonny: Tools  Options  Interpreter
     Select MicroPython (Rasberry Pi Pico)
     Install or update MicroPython, variant H or HW
In thonny REPL:
  print ( “Hello” )

## Slide 14
(rename serial port)

## Slide 15
Demo on-board blinky
In Thonny REPL:
In Tonny editor:

## Slide 16
Startup
boot.py runs first (at reset or power-up)
REPL STOP is a reset, and re-runs boot.py,
keyboard interrupt doesn’t re-run boot.py
Don’t mess with boot.py unless you really know what you are doing
main.py file runs after boot.py
REPL STOP doesn’t re-run main.py
keyboard interrupt doesn’t re-run main.py either
Put your startup line (import myapp.py) in main.py

## Slide 17
Demo startup
Save blink.py on the target
Create main.py on the target
Connect to power bank

## Slide 18
Demo external LED

## Slide 19
Demo input button

## Slide 20
Demo servo motor

## Slide 21
More LEDs!

## Slide 22
You still want more LEDs?

## Slide 23
3 ways
3 ways to work on and use a library
As (.py) sources
As (.mpy) pre-compiled code
As frozen (.mpy) code in the image
Compare using
Pi Pico RP2040 (without W)
MicroPython v1.19.1
Thonny for upload
My feeble laptop for building
My godafosss library code, with on-demand loading (85 files, 471 Kb, heavily commented)

## Slide 24
I still want more LEDs
Demo: Neopixels strip

## Slide 25
Some target chips/boards

## Slide 26
RAM
RAM is scarce, the Python is hungry
Split into smaller files to avoid peak RAM use
Use demand-loading (code)
Use pre-compiled files (mpy-cross)
Incorporate (pre-compiled) library files into the MicroPython image (demo)
Use a big fat fast target chip for development

## Slide 27
On-demand loading
from submodule import classname
def classname( *args, **kwargs ):
from submodule import classname
return classname(*args, **kwargs )
One trampoline takes ~ 50 bytes
The real code is a bit more complicated

## Slide 28
Limitations
Uses a lot of RAM, especially for an LCD graphic buffer
Speed is low (compared to running native code) and can be unpredictable (garbage collection)
Some timing-based HW interface protocols (neopixels, dallas one-wire, DHT11) are not feasible in native Python
Some doubts about running longer time (memory fragmentation), needs occasional 2nd start 
Needs more expensive hardware (than a native-code application)
Might use more power (than a native-code application)
Organization is MUCH smaller than python.org (hobbyistic)
Some standard libraries are not available and/or impractical (CPU & memory load)
Not all ports are equal (especially in WiFi details and built-in HW libraries)
No multi-threading (except when multiple CPUs are available)
Type hints not implemented yet

## Slide 29
Timing / performance
How much time do you have to do something simple?
1 - 10’s of CPU clock cycles: hardware peripherals, assembler, RP2040 PIO’s
10 - 100’s of CPU clock cycles: C, C++, Rust (or PicroPython built-in)
100’s - 1000’s of CPU clock cycles: MicroPython native
us
ms

## Slide 30
Deviations from CPython
Source: https://docs.micropython.org/en/latest/genrst

## Slide 31
Application areas
When faster development outweighs the extra hardware cost:
Tinkering (hobby, education, exploratory work, lab setting)
Prototyping, proof-of-concepts, demos
Testing
Small series
When a somewhat knowledgeable end-user must do some tweaking

## Slide 32
Caveats
Where is my code? Be sure to save your work on your PC (too)!
USB can supply only a limited amount of current
Upload, Download
Some chips claim MicroPython support but don’t fully deliver (W600, K210).
An uploaded file is sometimes not recognized as newer? (solution: add a space and upload again)
Thonny sometimes crashes (especially on communication problems – don’t pull the cable!)
Different MicroPython versions and ports can be subtly different (like no neopixel support on Teensy)
Want to protect your IP? Probably forget it.

## Slide 33
Not covered
Wireless REPL (WiFi)
Embedding native compiled code in the interpreter
Thonny alternatives
CircuitPython: proprietary variation by AdaFruit, very similar but some (irritating) differences
Extending MicroPython by embedding native code in the interpreter (C, C++)
Using MicroPython with RP2040 PIOs
Native code generators (@micropython.native, @micropython.viper)

## Slide 34
Takeaway?
Get
Arduino peripherals set (cheap!)
Pi RP2040 (or ESP32, Teensy 4.1)
Start tinkering!